7800 E. Michigan Ave.

Kalamazoo, Michigan  49048

Phone: (800) 521-2546

Fax: (269) 381-3455

www.landscapeforms.com

specify@landscapeforms.com

Harvest Bench and Table

Product Guide Specification

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition.

The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.

Section numbers are from MasterFormat 2010 Edition.

SECTION 12 93 43   SITE SEATING AND TABLES

SECTION 12 93 43.13   BENCHES

Specifier Notes:  This section covers Landscape Forms, Inc. "Harvest" bench and table.  Consult Landscape Forms, Inc. for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Bench and Table.

1.2	REFERENCES

Specifier Notes:  List standards referenced in this section, complete with designations and titles.  Delete standards not included in the edited section.  This article does not require compliance with standards, but is merely a listing of those used.

A.	ASTM Testing Standards:

1.	ASTM B 117 – Standard Practice for Operating Salt Spray (Fog) Apparatus.

2.	ASTM D 522 – Standard Test Methods for Mandrel Bend Test of Attached Organic Coatings.

3.	ASTM D 523 – Standard Test Method for Specular Gloss.

4.	ASTM D 2247 – Standard Practice for Testing Water Resistance of Coatings in 100% Relative Humidity.

5.	ASTM D 2794 – Standard Test Method for Resistance of Organic Coatings to the Effects of Rapid Deformation (Impact).

6.	ASTM D 3359 – Standard Test Methods for Measuring Adhesion by Tape Test.

7.	ASTM D 3363 – Standard Test Method for Film Hardness by Pencil Test.

8.	ASTM G 155 – Standard Practice for Operating Xenon Arc Light Apparatus for Exposure of Non-Metallic Materials.

B.	ISO Testing Standards:

1.	ISO 1520 – Paints and Varnishes – Cupping Test.

2.	ISO 2815 – Paints and Varnishes – Buchholz Indentation Test.

1.3	SUBMITTALS

A.	Product Data: Submit manufacturer’s product data, storage and handling requirements and recommendations, installation methods and available colors, styles, patterns and textures.

B.	Shop Drawings: Submit manufacturer’s shop drawings, including plans and elevations, indicating overall dimensions.

C.	Samples:  Submit manufacturer’s samples of materials, finishes, and colors.

D.	Warranty: Manufacturer’s standard warranty.

1.4	QUALITY ASSURANCE

A.	Manufacturer’s Qualifications: Manufacturer regularly engaged in manufacture of site furnishings since 1969.

B.	Product Support: Products are supported with complete engineering drawings and design patents.

C.	Base Worth: An installed base of products worth in excess of one hundred million dollars.

D.	Assets: Excess of twenty million dollars in assets.

E.	Production: Orders are filled within a 40-day schedule.

F.	Facility Operator: Welders and machine operators are certified.

1.5	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer’s original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage: Store materials in clean, dry area in accordance with manufacturer’s instructions.  Keep materials in manufacturer’s original, unopened containers and packaging until installation.

C.	Handling:  Protect materials and finish during handling and installation to prevent damage.

1.6	WARRANTY

A.	Warranty Information:

-Products will be free from defects in material and/or workmanship for a period of three years from the date of invoice.

-The warranty does not apply to damage resulting from accident, alteration, misuse, tampering, negligence, or abuse.

- Landscape Forms, Inc. shall, at its option, repair, replace, or refund the purchase price of any items found defective upon inspection by an authorized Landscape Forms service representative.

-Purchasers should be aware that normal use of these high quality products can result in superficial damage affecting the finish.  Scratches, nicks, and dents are to be considered normal wear and tear, and are not the responsibility of the manufacturer.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	Landscape Forms, Inc., 7800 E. Michigan Ave, Kalamazoo, Michigan 49048.                       Phone: (800) 521-2546. Fax (269) 381-3455.  Website www.landscapeforms.com                       E-mail:  specify@landscapeforms.com

2.2	BENCH and TABLES

A.	Harvest:

B.	Style:

1.	Bench

a.	Dining ht, 15-1/4” x 18-3/4” h

1)	46in length

2)	94in length

b.	Standing ht, 21” w x 29” h

1)	46in length

2.	Table

a.	Dining ht, 47-3/4” w x 94-3/4” l x 30-1/4” h

b.	Standing ht, 36-3/4” w x 94-3/4” l x 40” h

3.	Mounting:

a.	Freestanding

b.	Surface mount

3.	Accessories for table:

a.	Harvest luminaire, 6” height

b.	harvest luminaire, 14-1/4” height

4.	Accessories for standing ht bench:

a.	No bag hanger

b.	With bag hangers

5.	Optional surface mount:  anchoring hardware not included. (4) anchors per unit required, max Ø7/16” dia non-corrosive anchors recommended.

2.4	MATERIALS

A.	Bench seat and tabletop: 100% recycled high-density polyethylene (HDPE) with UV stabilizer and embedded pigmentation. Brass inserts in panels accept Magni-coated carbon steel bolts for attaching to frame.

B.	Bench seat and tabletop support frame: Formed 14 gauge A1008 CR type B or A1011 HRP&O type B carbon steel sheet, bolted to seat panels with Magni-coated screws.

C.	Frame: Legs and cross braces are formed from 6063-T52 aluminum tube. Cross braces bolt to legs with Magni-coated socket head cap screws.

D.	Glides: Supertough nylon 6/6, attached to legs with Magni-coated screws.

E.	Surface mount tabs: 3/8” thick 6061 aluminum plate.

F.	Luminaire frame: 6061-T6 aluminum tube frame, bolted to table. Includes 16 gauge carbon steel driver tray and cord cover.

G.	Light Cartridge Assembly:  IP68, LED, 3200K, 92 CRI, 417 total lumens, 10.5W power consumption. Light cartridge assembly is bonded to luminaire frame with glazing adhesive.

H.     Driver Circuitry:

- Driver mounting tray: formed carbon steel sheet; Tray is bolted to table frame.

2.	Driver: Class 1 output; CE; IP66; Suitable for dry and damp locations; Input: 100-277VAC, 50/60Hz; Output: 18-36 VDC, 350mA max. Max 12.6 watts. Driver attached to plate with glazing adhesive.

- Wiring:  Cartridge is connected to driver via outdoor-rated cord with weatherproof connectors.

- Supply wiring:  Unit is provided with a 12’ long outdoor-rated 16/3 corded plug.

2.5	RECYCLED CONTENT   Units are 100% recyclable.

|  | Post-Consumer Content | Pre-Consumer Content |
| --- | --- | --- |
| Harvest dining bench, 94in length | 43% | 10% |
| Harvest dining bench, 46in length | 38% | 9% |
| Harvest standing bench, 46in length | 33% | 8% |
| Harvest dining table | 42% | 7% |
| Harvest standing table | 40% | 8% |
| Harvest luminaire | 10% | 5% |

2.6	FINISHES

Specifier Notes:  Delete all that do not apply.

A.	Finish on metal:  Landscape Forms, Inc. “Pangard II”.

1.	Primer:  Rust inhibitor.

2.	Topcoat:  Thermosetting polyester powdercoat.  UV, chip, and flake resistant.

3.	Test Results:  “Pangard II”.

a.	Gloss, Garner 60 Degrees, ASTM D 523:  Plus or minus 5.

b.	UV Resistance, Color and Gloss, ASTM G 155, Cycle 7:  Delta E less than 2 at 2.0 mils and less than 20 percent loss.

c.	Cross-Hatch Adhesion, ASTM D 3359, Method B:  100 percent pass.

d.	Flexibility Test, Mandrel, ASTM D 522:  3 mm at 2 mils.

e.	Erichsen Cupping, ISO 1520:  8 mm.

f.	Impression Hardness, Buchholz, ISO 2815:  95.

g.	Impact Test, ASTM D 2794:  60 inches/pound at 2.5 mils.

h.	Pencil Hardness, ASTM D 3363:  2H minimum.

i.	Corrosion Resistance, 1,500-Hour Test, ASTM B 117:  Max undercutting 1 mm.

j.	Humidity Resistance, 1,500-Hour Test, ASTM D 2247:  Max blisters 1 mm.

Specifier Notes:  Specify color of finish.  Consult Landscape Forms, Inc. for selection of standard colors and availability of custom colors.

4.	Support Frame Color:  ____________

5.	Luminaire Color:  ________________

Specifier Notes:  Specify color of polyethylene.  Consult Landscape Forms, Inc. for selection of standard colors.

B.	Seat color / top color:  ________________________

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive units.

B.	Notify Architect of conditions that would adversely affect installation or subsequent use.

C.	Do not begin installation until unacceptable conditions are corrected.

3.2	INSTALLATION

A.	Install unit in accordance with manufacturer’s instructions at locations indicated on the Drawings.

B.	Install unit plumb and level.

3.3	ADJUSTING

A.	Finish Damage: Repair minor damages to finish in accordance with manufacturer’s instructions and as approved by Architect.

B.	Component Damage: Remove and replace damaged components that cannot be successfully repaired as determined by Architect.

3.4	CLEANING

A.	Clean unit promptly after installation in accordance with manufacturer’s instructions.

B.	Do not use harsh cleaning materials or methods that could damage finish.

3.5	PROTECTION

A.	Protect installed unit to ensure that, except for normal weathering, products will be without damage or deterioration at time of Substantial Completion.

END OF SECTION